# Data format
## Input data format

Illustration 1: Input data format

The program accepts data in the form of .xls or .xlsx (excel spreeadsheet) file with the following format:
- COLUMNS - samples of the experimental model to be analysed. First-row should contain a name of each sample for one column.
- ROWS - reference and target genes for analysis (selection is done inside the program). The first column should contain a name for the gene in a given row. Genes should be organized in continuous blocks and if pipetting control is used (multiple repetitions form the same sample), then these repetitions should also be one below the other (number of repetitions is selected inside the program).
- VALUES - For 'combined input' data values are expected to be Ct values.

# Interface
## Main Window

Illustration 2: Main window
- A – Menu from which we can perform 2 actions:
  - Read from combined input – a method for loading data into the program
  - Load Quantified – a method for loading quantified data, this action can be performed only after normal data is loaded.
- B – Input data section for displaying information about loaded data. "Show ***" buttons can be used to look up loaded information in the form of tables.
- C - Parameters section for selecting parameters for the algorithm. This section is active only after the input data is properly loaded.
  - 1) Selection of statistical models with the confidence value for evaluating if the difference between samples for a given target gene is statistically significant.
  - 2) Selecting the repetition number of removing the worst reference gene from the list passed to the normalization algorithm.
  - 3) A number of pipetting controls.
  - 4) Checkbox for selecting algorithm mode:
    - checked – for each remove repetition series only remove with best stability score will be selected for further analysis,
    - unchecked – all remove repetition levels will be used.
- D - Run calculations button - this action will be available only if input data is loaded and a proper parameters are selected
- E - Results summary section
  - 1) List displaying calculated coherence score for each target gene and all target genes average.
  - 2) Export results in form of single excel file
  - 3) Export results in form of boxplots graphs in the form of separate .png files for each target gene-remove repetition.

## Load input data window

Illustration 3: Load input data window

- A - Section for selecting the file from the drive to load (Select file)
- B - Section for selecting which genes should be used as reference genes. After selecting the gene from the available gene list (left window) press the "Select as ref->" button to add this gene to the reference gene list. Unselected genes are assumed to be target genes.
- C - Selection of samples models combinations. For automatic generation press "Generate combinations" which will generate all possible combinations of samples. For manual addition of model form list of possible samples use the "Add single" button.

After a successful file load, selecting a target and reference genes and models use "Accept" to load this data to the main application.
# Standard use case
1. From "File" menu select "Read from combined input" to open the window for loading data.
2. In "Read from combined input" use "Select file" button to load data from the spreadsheet.
3. In "Select reference genes" select reference genes to be used in analyze, unselected genes are assumed to be target genes.
4. In "Select Models" section create models of samples.
5. Use "Accept" button to load data into program memory and return to main window.
6. * If quantified data is available it can be loaded using “File → Load Quantified”
7. "Parameters" section set parameters for analysis.
8. Press "Run calculations" to perform analysis.
9. Export results in form of excel spreadsheet using "Export results" or as boxplot representation using "Export graphs".

If you use this software, please cite it as below:
1. Janik ME, Szwed S, Grzmil P, Kaczmarek R, Czerwiński M, Hoja-Łukowicza D. RT-qPCR analysis of human melanoma progression-related genes – A novel workflow for selection and validation of candidate reference genes. Int. J. Biochem. Cell Biol. 101 (2018) 12–18; doi: https://doi.org/10.1016/j.biocel.2018.05.007.
2. Hoja-Łukowicz D, Maciążek D, Janik M.E. Suitable reference genes selection for reliable normalization of gene expression in melanoma: implementation of an innovative GenExpA software. bioRxiv 2021.05.10.443386; doi: https://doi.org/10.1101/2021.05.10.443386.